## Slide 1: Carbon Efficiency
Green Software Use on HPC

## Slide 2: Questions
What does the term carbon equivalence (CO2e) mean?
Can we also have positive emissions impacts from HPC systems?
Objectives
Understand what CO2e means.
Appreciate positive emissions impacts from HPC systems.

## Slide 3: Greenhouse Gases
Greenhouse Gases (GHG) are gases that contribute to global warming and climate change.
Non-fluorinated gases
carbon dioxide, CO2
methane, CH4
nitrous oxide, N2O
fluorinated gases
hydrofluorocarbons, HFCs
perfluorocarbons, PFCs
sulphur hexafluoride, SF6
nitrogen trifluoride, NF3
In the atmosphere, these gases have different lifetimes and absorb different amounts of solar energy.

## Slide 4: Carbon equivalence
Each GHG has its own Global Warming Potential (GWP) that measures the relative potency of a gas as regards global warming.
Carbon dioxide has the lowest warming potential, it is the most abundant and lasts for thousands of years. For those reasons, CO2 is used as the reference for all other GHGs.
CO2 has a GWP of 1.
For example, over a 100-year timescale, one tonne of nitrous oxide has a global warming impact equivalent to that caused by 273 tonnes of CO2.
The GWP100 of N2O can be expressed in terms of a carbon equivalence, 273 CO2e.
Other abbreviations are sometimes used, CO2eq, CO2-eq, or simply "carbon”.
The concept of carbon dioxide equivalent allows us to compare the global warming potential of different GHGs.

## Slide 5: Carbon Efficiency in HPC
We aim to procure, run and use our HPC services in a way that minimises carbon emissions.
HPC systems commonly host research activities that can have a positive impact on emissions, e.g.
running climate models to provide the evidence to justify carbon reduction policies;
modelling wind farms and energy storage technologies to gain insights in how to improve real-world efficiency.
However, the benefits of such activities are difficult to quantify
HPC sites can be managed in ways that benefit the local environment, e.g.
redirecting waste heat to reduce the energy needs of homes and businesses,
  the waste energy of the LUMI supercomputer is used to heat a city
improving the biodiversity of surrounding land.
  Improving the sustainability of the ARCHER2 supercomputing service

## Slide 6: Exercise: carbon emissions from HPC systems
What do you think the sources of carbon emissions may be from HPC systems?
Write down 2-3 ideas of where you think emissions may come from.

## Slide 7: Solution
You may have come up with the following sources.
Emissions from electricity generation to power the HPC system.
Embodied emissions from manufacturing the HPC system components such as processors, memory and storage.
Embodied emissions from constructing the infrastructure required to house the HPC system.
Emissions associated with the people working to procure, run and support the HPC system.

## Slide 8: Exercise: Positive carbon impacts
Write down the activities that you do as part of your research or work that could be producing positive carbon impacts.
Can you order these activites by size of impact, from largest to smallest?

## Slide 9: Solution
Amongst other things, you may have come up with the following activities
The research or work you are engaged in is developing new innovations and technologies to reduce or eliminate emissions.
The research or work you are engaged in is providing data that is critical to efforts to quantify climate change and/or net zero strategies.
You are involved in training, education and/or activities raising awareness of carbon emissions and helping others to reduce their emissions.
You are developing resources and tools that help others to quantify and reduce their emissions.

## Slide 10: Quantifying positive impacts
Quantifying positive emissions impacts are often even more difficult than quantifying the (negative) emissions we produce through our work. Nevertheless, this work is critical to understanding how we are helping to meet climate commitments.
Example:
attending this course may motivate you to take some action that reduces the emissions associated with your work.
Maybe everyone attending this course resolves to take action to reduce their overall emissions by 2% this year, but this can be difficult for some, so perhaps only half actually manage to achieve this level of impact.
This still means however that overall, we would see a 1% reduction in emissions for this year per person attending the course.
If we assume that the work emissions per person per year are 6,000 kgCO2e, we could estimate that this course saves 60 kgCO2e per person attending.

## Slide 11: Key Points
CO2e is a measurement term used to measure the impact of all greenhouse gases.
Some activities we undertake on HPC systems can potentially have positive carbon impacts but these can be very difficult to quantify.
Everything we do emits carbon into the atmosphere, and our goal is to emit the least amount of carbon possible. This constitutes the first principle of green HPC system use: carbon efficiency, emitting the least amount of carbon possible per unit of work.